DY50 Wheel Loader

Compact design, low centre of gravity, tight turning radius and powerful performance – these features have characterized the TAIAN DY25/35/50 farm loader lines of products for years and still determine the immense success of the machines. The DY25/35/50 farm loader effortlessly fulfil any work task and work quickly, flexibly and safely – DY25/35/50 farm loader is simply always ready for use.

Features:

- Optional Euro stage V / EPA Tier 4 Engine;

- Hydrostatic 4 Wheel Drive;

- CE certified;

- Double Floating Functions;

- Quick Coupling System;

- Hand brake and pedal brake system;

- Side-Tilting Cabin;

- Multiple Attachments for customers’ choice;

Main Components:

- PWG brand driving pump, wheel motor and inch pedal;

- Multi-functional joystick;

- Bucher brand Multi Way Valve;

- Two way hydraulic output on the front end;

DY50 Cabins:

DY50 with Proof Canopy as standard, optional with Closed cabin and Collapsible Canopy cabin. The tiltable cabin design ensure the daily maintenance more easier.

DY50 Optional Engines:

| Engine Brand / Model | Yunnei DEF20CDF4 | Yanmar 4TNV88C |
| --- | --- | --- |
| Emissions | Euro V | Euro V / EPA Tier 4 |
| Cooling System | Water Cooling | Water Cooling |
| Cylinders | 4 Cylinders | 4 Cylinders |
| Rated Power | 45KW (61HP) | 34.3KW (46.6HP) |
| R.P.M. | 2600r/min | 2800r/min |

DY50 Specifications

| Model | DY50 |
| --- | --- |
| Overall Dimensions(With standard bucket): | 4850MM*1560MM*2340MM |
| Operating Weight (Without Attachment): | 2860kgs |
| Max. Lifting Height to the Pin (L): | 3264mm |
| Max.Lifting Force: | 2480kgs |
| Rated Loading Capacity (Bucket/Forks): | 1400kgs/1250kgs |
| Tipping Load With Standard Bucket: | 1680kgs |
| Oil Tank Capacity: |
| Fuel Tank Capacity: | 50L |
| Hydraulic Oil Tank Capacity: | 55L |
| Driving System: |
| Driving Speed: | 0-10km/H, 0-24 km/H |
| Type of Drive/Traction Drive: | Hydrostatic Via Drive Shaft |
| Pressure: | 400bar |
| Hydraulic Output: | 128L/min |
| Standard Tires: | 19.0/45-17 |
| Hydraulic Working System: |
| Hydraulic Output: | 89L/min |
| Working Pressure: | 180bar |
| Bucket Capacity: | 0.6CBM |

*The information and images in this document are provided for illustrative purpose only and do no bind the manufacturer, who reserves the right to make modifications at any time without prior warning.

DY50 Dimensions

| A | 1733mm | E | 4850 | J | 2548mm | N | 441mm |
| --- | --- | --- | --- | --- | --- | --- | --- |
| B | 730mm | F | 1360mm | K | 3059mm | O | 47° |
| C | 1196mm | G | 37mm | L | 3264mm | P | 40° |
| D | 3779mm | H | 2340 | M | 4036mm | Q | 47° |
| R | 1120mm | S | 1560mm | T | 252mm |  |  |
| U | 850mm | V | 2460mm | W | 2679mm | Y | 43° |

| DY50 FOB Qingdao China Unit Price: |
| --- |
| With Yunnei Euro V Engine: | USD22600.00 |
| With Yanmar Euro V / EPA Tier 4 Engine: | USD20300.00 |
| Basic Version: |
| Proof Canopy Cabin: | As standard |
| Quick Hitch: | As standard |
| Standard Bucket: | 1PC |
| Trailer Hook: | As standard |
| Counterweight: | As standard |
| Options: |
| Closed Cabin with A/C system: |
| Collapsible Canopy Cabin: |
| Pallet Fork: |

REMARKS:

1.HS Code:842951000;

2.Payment:30% T/T in advance, the rest T/T before shipment; Or irrevocable L/C at sight;

3.Delivery time:Within 30 days after receiving the deposit based on engines brand;

4.Packing:1 sets/1*20’GP; 3 sets/1*40’HQ.

5.Price Valid:40 Days.

**********************************************************************